## Slide 1
CORE COMPONENT
Network Infrastructure, Cabling and Unified Communications
Core Paper 1
Specification reference: 2.1, 2.2, 2.3
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
CORE COMPONENT · Core Paper 1
Learning objectives
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
2
By the end of this lesson you should be able to:
1
Interpret routing table data and TCP/IP configuration from console tools.
2
Explain what a firewall does and how ALLOW and BLOCK rules take precedence.
3
Compare cable types and Ethernet standards on bandwidth and length.
4
Explain VoIP, SIP, codecs and the network metrics that affect call quality.
STARTER
Open a command prompt and type ipconfig (or ifconfig on Linux or macOS). What do you think each line of the output tells you?

## Slide 3
CORE COMPONENT · Core Paper 1
Reading a routing table
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
3
Field | What it tells you
Network ID | The destination network the route leads to
Subnet mask | Which part of the address identifies the network
Next hop | The next router the packet is sent to
Interface | Which network interface the packet leaves through
Static or dynamic | Whether the route was entered by hand or learned from a routing protocol
Notes: Show a real routing table with 'route print' on Windows or 'ip route' on Linux.

## Slide 4
CORE COMPONENT · Core Paper 1
Console tools and firewalls
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
4
ipconfig / ifconfig: shows IP address, subnet mask, default gateway and DNS servers.
Firewall: filters traffic in and out of a network or device using rules.
Rules: each rule ALLOWs or BLOCKs traffic by address, port or application.
Precedence: rules are checked in order, and the first matching rule usually wins.
Admin access: secure it with strong credentials and restrict where it can be reached from.
!
KEY IDEA
Put specific rules above general ones. A 'block all' rule at the top would stop every rule below it from ever being reached.
Notes: Demonstrate ordering with two rules: ALLOW port 443 from anywhere, then BLOCK all.

## Slide 5
CORE COMPONENT · Core Paper 1
Cable types
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
5
1
UTP
Unshielded twisted pair. Cheap and flexible; the standard for office LANs.
2
STP
Shielded twisted pair. Extra shielding reduces interference in electrically noisy areas.
3
Coaxial
Copper core with a braided shield. Used for broadband and TV connections.
4
Fibre optic
Sends light, not electricity. Very high bandwidth over long distances and immune to interference.

## Slide 6
CORE COMPONENT · Core Paper 1
Ethernet cable standards
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
6
Standard | Typical bandwidth | Max length | Trade-off
CAT 5e | Up to 1 Gbps | 100 m | Cheapest; fine for most desktops
CAT 6 | Up to 10 Gbps (up to about 55 m) | 100 m | Better crosstalk protection, costs more
CAT 7 | Up to 10 Gbps | 100 m | Fully shielded, thicker and harder to install
Ethernet is the family of wired LAN standards these cables are built for.
Notes: Check the latest values in the specification if a question asks for exact figures.

## Slide 7
CORE COMPONENT · Core Paper 1
Unified communications
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
7
1
VoIP
Voice over IP carries phone calls as data packets over a network.
2
SIP
Session Initiation Protocol sets up, manages and ends VoIP calls and video sessions.
3
Codecs
Compress and decompress media. MPEG-4 for video, MP3 for lossy audio, FLAC for lossless audio.
Notes: SIP is the signalling that starts and ends the call; VoIP is the voice data itself.

## Slide 8
CORE COMPONENT · Core Paper 1
What affects call quality
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
8
1
Speed
How fast data is transferred.
2
Bandwidth
How much data can be carried at once.
3
Latency
The delay before data arrives. High latency causes talk-over.
4
Jitter
Variation in latency. Causes choppy, robotic audio.
5
Packet loss
Packets that never arrive. Causes gaps and dropped words.

## Slide 9
CORE COMPONENT · Core Paper 1
Check your understanding
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
9
1
What does the next hop field in a routing table show?
2
Which cable type is immune to electrical interference?
3
What is the maximum length of a CAT 6 Ethernet run?
4
What does SIP do?
5
Which network metric causes choppy, robotic-sounding calls?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 10
CORE COMPONENT · Core Paper 1
Answers
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
10
1
What does the next hop field in a routing table show?
The next router a packet is sent to.
2
Which cable type is immune to electrical interference?
Fibre optic.
3
What is the maximum length of a CAT 6 Ethernet run?
100 metres.
4
What does SIP do?
Sets up, manages and ends VoIP and video sessions.
5
Which network metric causes choppy, robotic-sounding calls?
Jitter.
Notes: Talk through any answers the class found difficult.

## Slide 11
CORE COMPONENT · Core Paper 1
Activity: Diagnose the bad VoIP line
Digital Support and Security T Level · Network Infrastructure, Cabling and Unified Communications
11
15 minutes
Pairs
1
A sales team complains that calls keep breaking up and people talk over each other.
2
Identify which network metrics could explain each symptom.
3
Suggest two tests you would run to confirm your theory.
4
Recommend one cabling or configuration change and justify it.
SUCCESS CRITERIA
Links talk-over to latency
Links breaking up to jitter or packet loss
Tests are realistic, e.g. ping or a VoIP quality tool
Recommendation is justified

## Slide 12
CORE COMPONENT · Core Paper 1
Exit ticket
1
What would ipconfig tell you if a PC cannot reach the internet?
2
Why must firewall rules be placed in the right order?
3
Which codec would you pick to archive a recording without losing quality?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Core Paper 1: Problem Solving, Digital Support and Data
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/01-core-component/01-core-paper-1.md
Notes: Students answer on a sticky note or in the chat before leaving.