## Slide 1
CORE COMPONENT
Networks
Core Paper 2
Specification reference: 7.3
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
CORE COMPONENT · Core Paper 2
Learning objectives
Digital Support and Security T Level · Networks
2
By the end of this lesson you should be able to:
1
Compare network types, topologies and models.
2
Describe the layers of the OSI and TCP/IP models.
3
Explain packet structure, packet switching and error checking.
4
Match common protocols to their purpose and explain bandwidth and latency.
STARTER
When you load a web page, how many different devices do you think your request passes through?

## Slide 3
CORE COMPONENT · Core Paper 2
Why network, and at what scale?
Digital Support and Security T Level · Networks
3
Benefits and drawbacks
Share files, printers and internet access
Central management and backups
But: cost of equipment and expertise
But: malware and faults can spread
Network types
PAN: personal area, e.g. Bluetooth
LAN: one building or site
MAN: across a town or city
WAN: across countries, e.g. the internet

## Slide 4
CORE COMPONENT · Core Paper 2
Topologies and models
Digital Support and Security T Level · Networks
4
1
Star
Every device connects to a central switch. One cable fault affects one device.
2
Mesh
Devices connect to many others. Very resilient, but costly.
3
Tree
Stars connected in a hierarchy.
4
Logical vs physical
How data flows versus how cables are laid out.
5
Client-server and thin client
Servers provide services; thin clients rely on the server to do the processing.
6
Peer-to-peer
Every device is equal and shares resources.
Notes: Components: servers, clients, routers, switches and the internet connection or backbone. Connectivity can be wired (copper, fibre) or wireless (access points).

## Slide 5
CORE COMPONENT · Core Paper 2
The OSI and TCP/IP models
Digital Support and Security T Level · Networks
5
OSI layer | Job | TCP/IP layer
7 Application | Services for user applications | Application
6 Presentation | Formatting, encryption, compression | Application
5 Session | Opens and manages sessions | Application
4 Transport | Reliable delivery, ports | Transport
3 Network | Logical addressing and routing | Internet
2 Data link | MAC addresses, frames | Network
1 Physical | Cables and signals | Network

## Slide 6
CORE COMPONENT · Core Paper 2
Data packets
Digital Support and Security T Level · Networks
6
Header: source and destination address, packet number, protocol.
Payload: the actual data being sent.
Trailer: error checking data, such as a CRC.
Packet switching: packets take different routes and are reassembled in order.
Packet loss: congestion, faulty hardware or interference.
!
KEY IDEA
A cyclic redundancy check (CRC) lets the receiver detect packets damaged on the way. Damaged packets are requested again.

## Slide 7
CORE COMPONENT · Core Paper 2
Common protocols
Digital Support and Security T Level · Networks
7
Group | Protocols | Purpose
Web | HTTP, HTTPS | Transfer web pages; HTTPS encrypts them
Mail | SMTP, POP, IMAP | Send mail; download it; or keep it on the server
Routing | RIP, OSPF | Routers share routes with each other
Application | FTP, SFTP | Transfer files; SFTP securely
Application | DHCP, DNS | Assign IP addresses; turn names into IP addresses
Bandwidth is how much data can be sent at once; latency is the delay. Both affect performance.

## Slide 8
CORE COMPONENT · Core Paper 2
Check your understanding
Digital Support and Security T Level · Networks
8
1
Which network type covers a single building?
2
Which OSI layer handles routing?
3
What is a CRC used for?
4
Which protocol turns a domain name into an IP address?
5
What is the difference between bandwidth and latency?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 9
CORE COMPONENT · Core Paper 2
Answers
Digital Support and Security T Level · Networks
9
1
Which network type covers a single building?
LAN.
2
Which OSI layer handles routing?
Layer 3, the network layer.
3
What is a CRC used for?
Detecting errors in transmitted packets.
4
Which protocol turns a domain name into an IP address?
DNS.
5
What is the difference between bandwidth and latency?
Bandwidth is capacity; latency is delay.
Notes: Talk through any answers the class found difficult.

## Slide 10
CORE COMPONENT · Core Paper 2
Activity: Follow the packet
Digital Support and Security T Level · Networks
10
20 minutes
Groups of seven
1
Each student is one OSI layer.
2
Pass a 'message' down the layers on the sending side, each adding its own header note.
3
Pass it up the layers on the receiving side, each removing its header.
4
Discuss which layer would notice each of these faults: unplugged cable, wrong IP, blocked port.
SUCCESS CRITERIA
Layers are in the right order
Each layer's job is described correctly
Faults matched to the right layer

## Slide 11
CORE COMPONENT · Core Paper 2
Exit ticket
1
Why is a star topology popular in offices?
2
Which layer do switches work at?
3
Name the protocol you would use to send an email.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Core Paper 2: Legislation, Business, Emerging Issues, Environments and Security
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/01-core-component/02-core-paper-2.md
Notes: Students answer on a sticky note or in the chat before leaving.