## Slide 1
DIGITAL INFRASTRUCTURE
Network Design, Addressing and Transmission
Digital Infrastructure Content Area 2
Specification reference: 2.1, 2.2
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Learning objectives
Digital Support and Security T Level · Network Design, Addressing and Transmission
2
By the end of this lesson you should be able to:
1
Explain resilience principles: high availability, clustering, load balancing and segmentation.
2
Explain Quality of Service and convert between number systems for addressing.
3
Compare copper, fibre and wireless transmission and their risks.
4
Describe IPv4 subnetting and IPv6 address types.
STARTER
A company's single web server crashes every Black Friday. Suggest two ways to keep the website up.

## Slide 3
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Designing for resilience
Digital Support and Security T Level · Network Design, Addressing and Transmission
3
1
High availability
Primary and secondary systems, so one can take over.
2
Clustering
Several servers act as one: redundancy and scalability.
3
Load balancing
Spreads traffic across servers.
4
Segmentation
Splits networks, systems and data to limit the impact of a problem.
Notes: QoS (Quality of Service) guarantees a level of service for important traffic such as VoIP.

## Slide 4
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Number systems for addressing
Digital Support and Security T Level · Network Design, Addressing and Transmission
4
System | Base | Example (decimal 255) | Used for
Binary | 2 | 11111111 | Subnet masks and IP calculations
Decimal | 10 | 255 | Dotted decimal IPv4 addresses
Hexadecimal | 16 | FF | IPv6 addresses and MAC addresses
Octal | 8 | 377 | Linux file permissions

## Slide 5
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Transmission media
Digital Support and Security T Level · Network Design, Addressing and Transmission
5
Copper and fibre
Copper carries electrical signals
Fibre carries light
Risks: tampering and signal loss
Separate copper from power cables to avoid EMI, static and crosstalk
Use shielding or planned parallel runs (BS EN 50174)
Wireless
802.11b, g and n
Wi-Fi 5 (802.11ac)
Wi-Fi 6 and 6E (802.11ax)
Wi-Fi 7 (802.11be)
Each generation raises speed and capacity

## Slide 6
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
IPv4 and IPv6
Digital Support and Security T Level · Network Design, Addressing and Transmission
6
IPv4
32-bit address, e.g. 192.168.1.10
Subnet mask splits network and host, e.g. /24
Subnetting divides a network into smaller ones
Private ranges, e.g. 10.0.0.0/8
IPv6
128-bit address in hexadecimal
Unicast: one interface
Multicast: a group
Anycast: the nearest of a group
Link-local and global addresses
Notes: Practise: how many hosts does a /26 give? (2 to the power 6, minus 2 = 62).

## Slide 7
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Check your understanding
Digital Support and Security T Level · Network Design, Addressing and Transmission
7
1
What does load balancing do?
2
Convert decimal 255 to binary.
3
Why keep data cables away from power cables?
4
How many bits in an IPv6 address?
5
How many usable hosts in a /24 subnet?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Answers
Digital Support and Security T Level · Network Design, Addressing and Transmission
8
1
What does load balancing do?
Spreads traffic across several servers.
2
Convert decimal 255 to binary.
11111111.
3
Why keep data cables away from power cables?
To avoid electromagnetic interference.
4
How many bits in an IPv6 address?
128.
5
How many usable hosts in a /24 subnet?
254.
Notes: Talk through any answers the class found difficult.

## Slide 9
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Activity: Subnet the office
Digital Support and Security T Level · Network Design, Addressing and Transmission
9
25 minutes
Individual
1
You have 192.168.10.0/24 for an office with four departments of up to 50 devices each.
2
Choose a subnet mask that gives four subnets.
3
Write the network address, first and last host and broadcast for each.
4
Suggest which resilience principle would protect the file server.
SUCCESS CRITERIA
Uses /26 correctly
Ranges do not overlap
Resilience choice is justified

## Slide 10
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Exit ticket
1
What is the difference between clustering and high availability?
2
Convert 1010 binary to decimal.
3
Name one improvement in Wi-Fi 6 over Wi-Fi 5.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Digital Infrastructure - Physical and Virtual Infrastructure
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/digital-infrastructure/02-physical-and-virtual-infrastructure.md
Notes: Students answer on a sticky note or in the chat before leaving.