## Slide 1
NETWORK CABLING
Cable Media, Connectors and Standards
Network Cabling Content Area 2
Specification reference: 2.11 to 2.16
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
NETWORK CABLING · Network Cabling Content Area 2
Learning objectives
Digital Support and Security T Level · Cable Media, Connectors and Standards
2
By the end of this lesson you should be able to:
1
Compare copper and fibre media types and their uses.
2
Explain the benefits of plenum-rated cable.
3
Identify connectors, transceivers and termination points.
4
Apply copper and fibre standards and termination methods.
STARTER
Why is most office cabling copper, but most links between buildings fibre?

## Slide 3
NETWORK CABLING · Network Cabling Content Area 2
Copper and fibre
Digital Support and Security T Level · Cable Media, Connectors and Standards
3
Copper
Durable, easy to handle, cheap to install
Can carry power (PoE)
Max 90 m permanent link, 100 m channel
UTP, STP, FTP, coaxial
Fibre
Longer distances, higher bandwidth
Lightweight, less degradation
Limited by the laser quality at each end
Single-mode OS1/OS2; multi-mode OM3/OM4
Notes: Plenum-rated cable gives off less smoke and toxic fumes, burns less, keeps working at higher heat, and complies with the Construction Products Regulation (CPR).

## Slide 4
NETWORK CABLING · Network Cabling Content Area 2
Connectors and transceivers
Digital Support and Security T Level · Cable Media, Connectors and Standards
4
1
Copper connectors
RJ-45, RJ-11, BNC, DB-9, DB-25, F-type.
2
Fibre connectors
LC, ST, SC, MT-RJ, MPO.
3
Choosing a connector
Mating type, locking (latch, screw, bayonet, APC or UPC), durability, size.
4
Transceivers
SFP, SFP+, GBIC, QSFP. Choose by duplex, bandwidth, WDM, rate and connector.

## Slide 5
NETWORK CABLING · Network Cabling Content Area 2
Termination points
Digital Support and Security T Level · Cable Media, Connectors and Standards
5
1
66 block
Punch-down for telephone systems; 22 to 26 gauge wire; Cat3.
2
110 block
Higher speeds (Cat5 to Cat6a); replaced the 66 block.
3
Patch panel
Incoming cables terminate at the back; patch leads connect at the front.

## Slide 6
NETWORK CABLING · Network Cabling Content Area 2
Copper cable standards
Digital Support and Security T Level · Cable Media, Connectors and Standards
6
Cable | Frequency (MHz) | Max length | Ethernet rate
Cat5e | 100 (up to 350) | 100 m | 1 Gbps (1000BASE-T)
Cat6 | 250 (up to 550) | 100 m | 1 or 10 Gbps
Cat6a | 500 (up to 550) | 100 m | 10 Gbps (10GBASE-T)
Cat7 | 600 | 100 m | 10 Gbps
RG59 / RG6 coax | High / low bandwidth | 229 m / 305 m | 10 Mbps
Notes: The full tables for Cat3 and Cat5 and for fibre OM1 to OM4 by wavelength are on the wiki page.

## Slide 7
NETWORK CABLING · Network Cabling Content Area 2
Termination methods and standards
Digital Support and Security T Level · Cable Media, Connectors and Standards
7
Methods
Patching to a patch panel
RJ45 for Ethernet
Fusion splicing: permanent, single-mode
Mechanical splicing: non-permanent, single or multi-mode
Standards
TIA/EIA-568A and 568B pin-outs
Straight-through: same standard at both ends
Crossover: 568A at one end, 568B at the other
Ethernet: 100BaseT through 10GBaseT

## Slide 8
NETWORK CABLING · Network Cabling Content Area 2
Check your understanding
Digital Support and Security T Level · Cable Media, Connectors and Standards
8
1
What is the maximum copper channel length?
2
Which fibre connector is small and common in switches?
3
What does plenum-rated cable reduce in a fire?
4
Which punch-down block supports Cat6?
5
What makes a crossover cable?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 9
NETWORK CABLING · Network Cabling Content Area 2
Answers
Digital Support and Security T Level · Cable Media, Connectors and Standards
9
1
What is the maximum copper channel length?
100 metres.
2
Which fibre connector is small and common in switches?
LC.
3
What does plenum-rated cable reduce in a fire?
Smoke and toxic fumes.
4
Which punch-down block supports Cat6?
The 110 block.
5
What makes a crossover cable?
568A at one end and 568B at the other.
Notes: Talk through any answers the class found difficult.

## Slide 10
NETWORK CABLING · Network Cabling Content Area 2
Activity: Spec the materials
Digital Support and Security T Level · Cable Media, Connectors and Standards
10
25 minutes
Pairs
1
Scenario: a two-storey office with 40 desks and a link to a warehouse 400 m away.
2
Choose cable types for the desks, riser and warehouse link.
3
Choose connectors, transceivers and termination points.
4
Justify each choice using the standards tables.
SUCCESS CRITERIA
Lengths stay within standards
Fibre type suits the 400 m link
Plenum cable considered where needed

## Slide 11
NETWORK CABLING · Network Cabling Content Area 2
Exit ticket
1
When would you use single-mode fibre?
2
Name two copper connectors.
3
What is the difference between fusion and mechanical splicing?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Network Cabling - Installation and Testing
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/network-cabling/02-cabling-installation-and-testing.md
Notes: Students answer on a sticky note or in the chat before leaving.