## Slide 1
NETWORK CABLING
Testing, Certification and Troubleshooting
Network Cabling Content Area 2
Specification reference: 2.17, 2.18, 2.26 to 2.29
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
NETWORK CABLING · Network Cabling Content Area 2
Learning objectives
Digital Support and Security T Level · Testing, Certification and Troubleshooting
2
By the end of this lesson you should be able to:
1
Apply a troubleshooting process to cabling faults.
2
Identify common physical and technical failures.
3
Test and certify copper and fibre to recognised standards.
4
Explain the consequences of poor workmanship.
STARTER
A new desk outlet only connects at 100 Mbps instead of 1 Gbps. What could cause that?

## Slide 3
NETWORK CABLING · Network Cabling Content Area 2
Troubleshooting process
Digital Support and Security T Level · Testing, Certification and Troubleshooting
3
1
Identify
A fault, or found in routine monitoring.
2
Diagnose
Gather info, compare with past data, narrow down.
3
Test
Test the shortlist.
4
Resolve
Fix, document and prevent recurrence.
Maintenance can be predictive (replace before failure) or reactive (run to failure).

## Slide 4
NETWORK CABLING · Network Cabling Content Area 2
Common failures
Digital Support and Security T Level · Testing, Certification and Troubleshooting
4
Physical
Wrong cable type or pin-out
Open or short circuit
Bad port, bent pins, cable damage
Duplex or speed mismatch
Wrong containment
Technical
Attenuation, latency, jitter
Crosstalk and EMI
Transceiver mismatch, TX/RX reversed
Bottlenecks and hardware errors
Spotted via CRC errors, lost packets, address conflicts

## Slide 5
NETWORK CABLING · Network Cabling Content Area 2
Testing standards
Digital Support and Security T Level · Testing, Certification and Troubleshooting
5
Standard | Covers
TIA/EIA-568-B.2-1 | Cat6 transmission performance
TIA/EIA-568-B.1-10 | Augmented Cat6
TIA/EIA-TSB-155-A | Cat6 support for 10GBASE-T
TIA-1152 | Field test instrument requirements
IEC 61935-1 | Reference measurement procedures

## Slide 6
NETWORK CABLING · Network Cabling Content Area 2
Certifying copper and fibre
Digital Support and Security T Level · Testing, Certification and Troubleshooting
6
Copper
Continuity tester, performance tester, certifier
Wiremap
Cable length
Near-end crosstalk (NEXT)
Fibre
OLTS, light source and power meter
OTDR
Fibre inspection scope
Tier 1 and tier 2 testing
Notes: Follow a test plan (scope, approach, resources, schedule), then interpret results against manufacturer tolerances.

## Slide 7
NETWORK CABLING · Network Cabling Content Area 2
Why poor workmanship matters
Digital Support and Security T Level · Testing, Certification and Troubleshooting
7
Network consequences
Slower speeds and more interference
Harder maintenance and shorter cable life
Weaker security
Bad labelling slows every future fault-find
Business consequences
Cost of revisits
SLA and warranty penalties
Reputational damage and delayed payment
Failed audits

## Slide 8
NETWORK CABLING · Network Cabling Content Area 2
Check your understanding
Digital Support and Security T Level · Testing, Certification and Troubleshooting
8
1
What is the difference between predictive and reactive maintenance?
2
Name two physical cabling failures.
3
What does NEXT stand for?
4
Which tool locates a break along a fibre?
5
Give one business consequence of failing certification.
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 9
NETWORK CABLING · Network Cabling Content Area 2
Answers
Digital Support and Security T Level · Testing, Certification and Troubleshooting
9
1
What is the difference between predictive and reactive maintenance?
Predictive replaces before failure; reactive runs to failure.
2
Name two physical cabling failures.
Any two, e.g. wrong pin-out, open circuit, bent pins.
3
What does NEXT stand for?
Near-end crosstalk.
4
Which tool locates a break along a fibre?
An OTDR.
5
Give one business consequence of failing certification.
E.g. revisit costs, SLA penalties, reputational damage.
Notes: Talk through any answers the class found difficult.

## Slide 10
NETWORK CABLING · Network Cabling Content Area 2
Activity: Fault-find the patch leads
Digital Support and Security T Level · Testing, Certification and Troubleshooting
10
30 minutes
Pairs, practical
1
Test the six numbered patch leads your teacher provides.
2
Record the wiremap and length result for each.
3
Identify the fault in each failing lead.
4
Write a short certification summary for the passing leads.
SUCCESS CRITERIA
Every lead tested and recorded
Faults named correctly, e.g. split pair, open
Results compared with tolerances
Notes: Prepare leads with a split pair, a reversed pair, an open conductor and one good lead.

## Slide 11
NETWORK CABLING · Network Cabling Content Area 2
Exit ticket
1
Why must every cable be tested, not just a sample?
2
What might cause a CRC error?
3
Why does labelling matter?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Network Cabling - Installation and Testing
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/network-cabling/02-cabling-installation-and-testing.md
Notes: Students answer on a sticky note or in the chat before leaving.