## Slide 1
CORE COMPONENT
Health and Safety in Digital Work
Core Paper 2
Specification reference: 4.1 (health and safety)
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
CORE COMPONENT · Core Paper 2
Learning objectives
Digital Support and Security T Level · Health and Safety in Digital Work
2
By the end of this lesson you should be able to:
1
Describe employer duties under the Health and Safety at Work Act.
2
Explain the manual handling, work at height and DSE regulations.
3
Identify the main health and safety risks of digital work.
4
Recommend suitable mitigations for each risk.
STARTER
Look around this room. List every hazard you can see that could hurt someone working in IT here.

## Slide 3
CORE COMPONENT · Core Paper 2
Health and Safety at Work Act
Digital Support and Security T Level · Health and Safety in Digital Work
3
The Health and Safety at Work Act is the main law protecting people at work, including in IT.
Employers must provide a safe working environment, train staff properly, provide adequate welfare facilities such as toilets and drinking water, and give the information, instruction and supervision people need to work safely.
Employees have duties too: take reasonable care of themselves and others, follow training and safety procedures, and not misuse safety equipment.
More specific regulations, such as those for display screens and manual handling, sit underneath it.
e.g.
EXAMPLE
A new technician must be trained before working in the server room, shown the fire exits and emergency power-off, and supervised until they're competent.

## Slide 4
CORE COMPONENT · Core Paper 2
Health and Safety at Work Act
Digital Support and Security T Level · Health and Safety in Digital Work
4
Provide a safe working environment
Train staff properly
Provide adequate welfare facilities
Give relevant information, instruction and supervision
!
KEY IDEA
Employers carry the main duty, but employees must also take reasonable care of themselves and others.
Notes: This is the umbrella law. The regulations on the next slides sit under it.

## Slide 5
CORE COMPONENT · Core Paper 2
Quick check: Health and Safety at Work Act
Digital Support and Security T Level · Health and Safety in Digital Work
5
1
Name two employer duties under the Act.
2
Do employees have duties too?
3
How do other regulations relate to the Act?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Any two: safe environment, training, welfare, information, instruction, supervision.
2. Yes: take reasonable care and follow safety procedures.
3. They sit under it and cover specific risks.

## Slide 6
CORE COMPONENT · Core Paper 2
Key regulations
Digital Support and Security T Level · Health and Safety in Digital Work
6
Manual handling regulations: avoid hazardous lifting where possible. Where you can't, assess the risk, tell staff about the load's weight and centre of gravity, and reduce the risk, for example with trolleys or team lifts.
Work at height regulations: avoid it where you can. Otherwise plan and supervise the work, use competent people and suitable, stable equipment, protect against falling objects and plan for emergencies.
Display screen equipment (DSE) regulations: employers must assess workstations, reduce risks including regular breaks from the screen, provide eye tests on request, and give training.
e.g.
EXAMPLE
Fitting a wireless access point on a 3 m ceiling: use a podium step or tower rather than a chair, have a second person present, and keep tools tethered.

## Slide 7
CORE COMPONENT · Core Paper 2
Key regulations
Digital Support and Security T Level · Health and Safety in Digital Work
7
1
Manual handling
Avoid hazardous lifting where possible. Otherwise assess the risk, give information on the load and its centre of gravity, and reduce the risk of injury.
2
Work at height
Plan and supervise the work, use competent people, do as much as possible from the ground, use suitable, stable equipment, protect against falling objects, plan for emergencies.
3
Display screen equipment
Assess workstations, reduce risks including regular breaks, provide eye tests on request, and give training and information.

## Slide 8
CORE COMPONENT · Core Paper 2
Quick check: Key regulations
Digital Support and Security T Level · Health and Safety in Digital Work
8
1
What is the first rule of the work at height regulations?
2
What must employers provide DSE users on request?
3
Give one way to reduce manual handling risk.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Avoid working at height where possible.
2. An eye test.
3. E.g. trolleys, team lifts, training.

## Slide 9
CORE COMPONENT · Core Paper 2
Risks in digital work and how to reduce them
Digital Support and Security T Level · Health and Safety in Digital Work
9
IT work has real physical risks.
Long hours at a screen cause eye strain and back, neck and wrist pain. Workstation assessments, adjustable chairs, correct screen height and regular breaks reduce this.
Cable installation risks trips, cuts from cable ties and trunking, and electric shock. Keep cables tidy, wear gloves and isolate power first.
Lifting servers and boxes of equipment risks back injury. Use trolleys and team lifts.
The four main mitigations are training, a safe environment and practices, safety equipment and supervision.
e.g.
EXAMPLE
A technician re-cabling a comms cabinet isolates power, wears gloves, uses a trolley for the new switch and routes cables away from walkways.

## Slide 10
CORE COMPONENT · Core Paper 2
Risks in digital work and how to reduce them
Digital Support and Security T Level · Health and Safety in Digital Work
10
Activity | Risk | Mitigation
Using DSE all day | Eye strain, back and wrist pain | Workstation assessment, breaks, eye tests
Working at height | Falls, dropped tools | Training, correct ladders or towers, supervision
Cable installation | Trips, cuts, electric shock | Safe environment, PPE, isolate power
Manual handling | Back injury from servers or boxes | Trolleys, team lifts, training
Notes: The four mitigation themes from the specification: training, safe environment, safety equipment and supervision.

## Slide 11
CORE COMPONENT · Core Paper 2
Quick check: Risks in digital work and how to reduce them
Digital Support and Security T Level · Health and Safety in Digital Work
11
1
Name two health risks of DSE work.
2
How can cable installation be made safer?
3
Name the four main mitigation themes.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Any two: eye strain, back, neck or wrist pain.
2. E.g. isolate power, wear gloves, keep cables tidy.
3. Training, safe environment, safety equipment, supervision.

## Slide 12
CORE COMPONENT · Core Paper 2
Key terms
Digital Support and Security T Level · Health and Safety in Digital Work
12
DSE display screen equipment, such as monitors and laptops.
Risk assessment identifying hazards and deciding how to control them.
PPE personal protective equipment, such as gloves or hard hats.
Competent person someone with the training and experience to do the task safely.

## Slide 13
CORE COMPONENT · Core Paper 2
Check your understanding
Digital Support and Security T Level · Health and Safety in Digital Work
13
1
Name two duties employers have under the Health and Safety at Work Act.
2
What must an employer provide on request under the DSE regulations?
3
What is the first rule of the Work at Height Regulations?
4
Give one mitigation for manual handling risks.
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 14
CORE COMPONENT · Core Paper 2
Answers
Digital Support and Security T Level · Health and Safety in Digital Work
14
1
Name two duties employers have under the Health and Safety at Work Act.
Any two of: safe environment, training, welfare provision, information, instruction and supervision.
2
What must an employer provide on request under the DSE regulations?
An eye test.
3
What is the first rule of the Work at Height Regulations?
Avoid working at height where possible; do as much as possible from the ground.
4
Give one mitigation for manual handling risks.
Trolleys, team lifts or manual handling training.
Notes: Talk through any answers the class found difficult.

## Slide 15
CORE COMPONENT · Core Paper 2
Activity: Risk assess a server room move
Digital Support and Security T Level · Health and Safety in Digital Work
15
20 minutes
Small groups
1
Your team is moving three rack servers and re-cabling a comms cabinet on a mezzanine floor.
2
Identify at least five hazards.
3
Link each one to the law or regulation that applies.
4
Suggest a mitigation for each.
SUCCESS CRITERIA
Covers lifting, height and electrical hazards
Correct regulation named for each
Mitigations are practical

## Slide 16
CORE COMPONENT · Core Paper 2
Exit ticket
1
Which regulation covers lifting a server?
2
Why do DSE users need regular breaks?
3
Name one hazard of installing cabling in a ceiling.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Core Paper 2: Legislation, Business, Emerging Issues, Environments and Security
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/01-core-component/02-core-paper-2.md
Notes: Students answer on a sticky note or in the chat before leaving.