## Slide 1
CORE COMPONENT
Virtual, Cloud and Resilient Environments
Core Paper 2
Specification reference: 7.4, 7.5, 7.6
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
CORE COMPONENT · Core Paper 2
Learning objectives
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
2
By the end of this lesson you should be able to:
1
Describe virtual machines, hypervisors and the benefits and drawbacks of virtualisation.
2
Compare private and public cloud and the IaaS, PaaS and SaaS models.
3
Explain methods to make a digital environment resilient.
STARTER
If your college's server room flooded tonight, what would still work tomorrow morning? What would not?

## Slide 3
CORE COMPONENT · Core Paper 2
Virtual environments
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
3
Virtualisation runs several virtual machines (VMs) on one physical computer, each behaving like a separate PC, server, switch or router.
A hypervisor manages them. A Type 1 hypervisor runs directly on the hardware and is used in data centres. A Type 2 runs on top of a normal OS, like VirtualBox on a laptop.
VMs are isolated, portable and easy to copy, so they're cost-effective at scale, easy to manage, and great for disaster recovery, testing and training.
The downsides: they put extra load on the hardware, run a little slower, and performance figures can be misleading.
e.g.
EXAMPLE
A college runs 40 student VMs on two physical servers. If a student breaks theirs, the technician restores it from a snapshot in minutes.

## Slide 4
CORE COMPONENT · Core Paper 2
Virtual environments
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
4
Components and features
Virtual machines: PCs, switches, routers, servers
Type 1 hypervisor runs directly on hardware
Type 2 hypervisor runs on top of an OS
Features: isolation, emulation, portability, sharing
Benefits and drawbacks
Cost-effective at scale and easy to manage
Resilient, better disaster recovery and testing
Possibly lower carbon footprint
But: extra load on hardware and slower execution
But: performance figures can be misleading

## Slide 5
CORE COMPONENT · Core Paper 2
Quick check: Virtual environments
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
5
1
What does a hypervisor do?
2
Where does a Type 1 hypervisor run?
3
Give one benefit of virtualisation.
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Creates and manages virtual machines.
2. Directly on the hardware.
3. E.g. lower cost at scale, easy recovery, safe testing.

## Slide 6
CORE COMPONENT · Core Paper 2
Cloud delivery models: who manages what?
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
6
Cloud computing rents computing resources over the internet. It can be public (shared provider infrastructure) or private (dedicated to one organisation). Its benefits are portability, elasticity (scaling up and down), fewer storage limits and cost.
The three delivery models differ in who manages what.
IaaS (Infrastructure as a Service): the provider supplies virtual hardware; you manage the OS and everything above it.
PaaS (Platform as a Service): the provider also manages the OS and runtime; you manage your applications and data.
SaaS (Software as a Service): the provider runs everything; you just manage users and data.
e.g.
EXAMPLE
Renting virtual servers on AWS is IaaS; deploying code to a managed app platform is PaaS; using Microsoft 365 is SaaS.

## Slide 7
CORE COMPONENT · Core Paper 2
Cloud delivery models: who manages what?
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
7
Model | Client manages | Provider manages
IaaS | Applications, OS and middleware, runtime, data, user accounts | Virtualisation and hardware
PaaS | Applications, data, user accounts | Hardware, virtualisation, OS and runtime
SaaS | User accounts and data | Everything else, including the application
Cloud can be private or public. Benefits: portability, elasticity, fewer storage limits, cost-effectiveness.

## Slide 8
CORE COMPONENT · Core Paper 2
Quick check: Cloud delivery models: who manages what?
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
8
1
In SaaS, what does the client manage?
2
Which model gives the client the most control?
3
What is elasticity?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. User accounts and data.
2. IaaS.
3. Scaling resources up and down as demand changes.

## Slide 9
CORE COMPONENT · Core Paper 2
Making environments resilient
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
9
A resilient environment keeps working, or recovers quickly, when something goes wrong. It improves security, protects reputation and reduces downtime.
Methods include: applying software updates and patches; replacing hardware on a rolling plan and disposing of old kit securely; building in redundancy so no single failure stops the service; hardening devices by removing unneeded ports, apps and permissions; backing up onsite, offsite and to the cloud with tested recovery procedures; and standard operating procedures with training so staff handle incidents consistently.
e.g.
EXAMPLE
A shop's card system uses two internet connections and a backup router. When the main line fails, sales continue on the backup.

## Slide 10
CORE COMPONENT · Core Paper 2
Making environments resilient
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
10
1
Patches and updates
Planned, and in response to new vulnerabilities.
2
Hardware replacement
Rolling plans and secure disposal.
3
Redundancy
Duplicate data and systems so one failure is not fatal.
4
Device hardening
Remove unneeded ports, apps, permissions and access.
5
Backups and recovery
Onsite, offsite and cloud; hot, warm or cold sites.
6
Standard procedures
Training, induction and careful rollout of new systems.
Notes: Benefits of resilience: better security, better reputation and less downtime.

## Slide 11
CORE COMPONENT · Core Paper 2
Quick check: Making environments resilient
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
11
1
What is redundancy?
2
What is device hardening?
3
Why keep a backup offsite?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Duplicate components so one failure doesn't stop the service.
2. Removing unneeded ports, apps and permissions.
3. So it survives a fire, flood or theft at the main site.

## Slide 12
CORE COMPONENT · Core Paper 2
Hot, warm and cold sites
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
12
If the main site is lost, organisations can move to a backup site. There are three types.
A hot site is fully equipped with up-to-date data, ready within minutes or hours. It's the most expensive.
A warm site has equipment in place but data must be restored first, taking hours to days.
A cold site is just space, power and connectivity, taking days or weeks to set up, but it's cheap.
The choice depends on how long the business can survive without its systems.
e.g.
EXAMPLE
A bank needs a hot site because minutes of downtime cost millions. A small charity might accept a cold site or rely on cloud services.

## Slide 13
CORE COMPONENT · Core Paper 2
Hot, warm and cold sites
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
13
Site | What it has | Recovery speed | Cost
Hot | Fully equipped with live, up-to-date data | Minutes to hours | High
Warm | Equipment in place, data needs restoring | Hours to days | Medium
Cold | Space and power only | Days to weeks | Low

## Slide 14
CORE COMPONENT · Core Paper 2
Quick check: Hot, warm and cold sites
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
14
1
Which site type is fastest to switch to?
2
What does a warm site need before use?
3
Why would a business choose a cold site?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. A hot site.
2. Data restored from backups.
3. It's the cheapest option if longer downtime is acceptable.

## Slide 15
CORE COMPONENT · Core Paper 2
Check your understanding
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
15
1
What is the difference between a Type 1 and Type 2 hypervisor?
2
In SaaS, what does the client manage?
3
What is device hardening?
4
Which disaster recovery site is fastest to switch to?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 16
CORE COMPONENT · Core Paper 2
Answers
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
16
1
What is the difference between a Type 1 and Type 2 hypervisor?
Type 1 runs directly on hardware; Type 2 runs on an operating system.
2
In SaaS, what does the client manage?
User accounts and data.
3
What is device hardening?
Removing unneeded ports, apps, permissions and access to reduce vulnerabilities.
4
Which disaster recovery site is fastest to switch to?
A hot site.
Notes: Talk through any answers the class found difficult.

## Slide 17
CORE COMPONENT · Core Paper 2
Activity: Choose a cloud model
Digital Support and Security T Level · Virtual, Cloud and Resilient Environments
17
20 minutes
Pairs
1
Three clients: a start-up building its own web app; a school wanting email; a company that needs full control of its servers.
2
Recommend IaaS, PaaS or SaaS for each.
3
Explain what each client would still be responsible for.
4
Suggest one resilience measure for each.
SUCCESS CRITERIA
Model matches the level of control needed
Responsibilities stated correctly
Resilience measure is realistic

## Slide 18
CORE COMPONENT · Core Paper 2
Exit ticket
1
Give one drawback of virtualisation.
2
Which cloud model gives the client the most control?
3
Why use offsite backups?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Core Paper 2: Legislation, Business, Emerging Issues, Environments and Security
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/01-core-component/02-core-paper-2.md
Notes: Students answer on a sticky note or in the chat before leaving.