## Slide 1
DIGITAL INFRASTRUCTURE
Network Design, Addressing and Transmission
Digital Infrastructure Content Area 2
Specification reference: 2.1, 2.2
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Learning objectives
Digital Support and Security T Level · Network Design, Addressing and Transmission
2
By the end of this lesson you should be able to:
1
Explain resilience principles: high availability, clustering, load balancing and segmentation.
2
Explain Quality of Service and convert between number systems for addressing.
3
Compare copper, fibre and wireless transmission and their risks.
4
Describe IPv4 subnetting and IPv6 address types.
STARTER
A company's single web server crashes every Black Friday. Suggest two ways to keep the website up.

## Slide 3
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Designing for resilience
Digital Support and Security T Level · Network Design, Addressing and Transmission
3
A resilient network keeps working when a part fails or demand spikes.
High availability pairs a primary system with a secondary that takes over automatically if the primary fails.
Clustering makes several servers act as one: if one fails the others carry on, and more can be added as demand grows.
Load balancing spreads incoming traffic across several servers so none is overwhelmed.
Segmentation splits the network, systems and data so a problem in one part stays there.
Quality of Service (QoS) guarantees bandwidth for important traffic, such as voice calls.
e.g.
EXAMPLE
An online shop runs three web servers behind a load balancer. On Black Friday traffic is shared out, and when one server crashes customers don't notice.

## Slide 4
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Designing for resilience
Digital Support and Security T Level · Network Design, Addressing and Transmission
4
1
High availability
Primary and secondary systems, so one can take over.
2
Clustering
Several servers act as one: redundancy and scalability.
3
Load balancing
Spreads traffic across servers.
4
Segmentation
Splits networks, systems and data to limit the impact of a problem.
Notes: QoS (Quality of Service) guarantees a level of service for important traffic such as VoIP.

## Slide 5
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Quick check: Designing for resilience
Digital Support and Security T Level · Network Design, Addressing and Transmission
5
1
What does a load balancer do?
2
What is high availability?
3
Why use QoS?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Spreads traffic across several servers.
2. A secondary system automatically taking over if the primary fails.
3. To guarantee bandwidth for important traffic such as voice.

## Slide 6
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Number systems for addressing
Digital Support and Security T Level · Network Design, Addressing and Transmission
6
System | Base | Example (decimal 255) | Used for
Binary | 2 | 11111111 | Subnet masks and IP calculations
Decimal | 10 | 255 | Dotted decimal IPv4 addresses
Hexadecimal | 16 | FF | IPv6 addresses and MAC addresses
Octal | 8 | 377 | Linux file permissions

## Slide 7
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Transmission media
Digital Support and Security T Level · Network Design, Addressing and Transmission
7
Data travels as electrical signals on copper, light pulses in fibre, or radio waves over wireless.
Copper can pick up interference: electromagnetic interference from power cables and motors, static, and crosstalk between neighbouring pairs. BS EN 50174 sets how far data cabling must be kept from power cabling, or requires shielding.
All media carry security risks: cables can be tapped and signals lost.
Wireless has evolved through 802.11b, g and n, then Wi-Fi 5 (ac), Wi-Fi 6 and 6E (ax) and Wi-Fi 7 (be). Each generation adds speed and handles more devices at once.
e.g.
EXAMPLE
Running a data cable alongside a power cable in the same trunking causes intermittent errors; separating them or using shielded cable fixes it.

## Slide 8
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Transmission media
Digital Support and Security T Level · Network Design, Addressing and Transmission
8
Copper and fibre
Copper carries electrical signals
Fibre carries light
Risks: tampering and signal loss
Separate copper from power cables to avoid EMI, static and crosstalk
Use shielding or planned parallel runs (BS EN 50174)
Wireless
802.11b, g and n
Wi-Fi 5 (802.11ac)
Wi-Fi 6 and 6E (802.11ax)
Wi-Fi 7 (802.11be)
Each generation raises speed and capacity

## Slide 9
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Quick check: Transmission media
Digital Support and Security T Level · Network Design, Addressing and Transmission
9
1
Name two sources of interference on copper.
2
Which standard covers segregating data and power cabling?
3
What is the IEEE name for Wi-Fi 6?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Any two: EMI, static, crosstalk.
2. BS EN 50174.
3. 802.11ax.

## Slide 10
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
IPv4 and IPv6
Digital Support and Security T Level · Network Design, Addressing and Transmission
10
IPv4 addresses are 32 bits, written as four decimal numbers such as 192.168.1.10. The subnet mask (such as 255.255.255.0, or /24) shows which part is the network and which part identifies the host.
Subnetting splits one network into smaller ones, improving security and reducing broadcast traffic. The number of usable hosts is 2 to the power of the host bits, minus 2 (the network and broadcast addresses).
IPv4 has run out of addresses, so IPv6 uses 128-bit addresses written in hexadecimal. Types include unicast (one device), multicast (a group) and anycast (the nearest of a group).
e.g.
EXAMPLE
192.168.10.0/26 leaves 6 host bits: 2 to the power 6 = 64, minus 2 = 62 usable addresses per subnet, giving four subnets from one /24.

## Slide 11
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
IPv4 and IPv6
Digital Support and Security T Level · Network Design, Addressing and Transmission
11
IPv4
32-bit address, e.g. 192.168.1.10
Subnet mask splits network and host, e.g. /24
Subnetting divides a network into smaller ones
Private ranges, e.g. 10.0.0.0/8
IPv6
128-bit address in hexadecimal
Unicast: one interface
Multicast: a group
Anycast: the nearest of a group
Link-local and global addresses
Notes: Practise: how many hosts does a /26 give? (2 to the power 6, minus 2 = 62).

## Slide 12
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Quick check: IPv4 and IPv6
Digital Support and Security T Level · Network Design, Addressing and Transmission
12
1
How many bits in an IPv4 address?
2
How many usable hosts in a /24?
3
Why was IPv6 introduced?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. 32.
2. 254.
3. IPv4 addresses have run out.

## Slide 13
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Check your understanding
Digital Support and Security T Level · Network Design, Addressing and Transmission
13
1
What does load balancing do?
2
Convert decimal 255 to binary.
3
Why keep data cables away from power cables?
4
How many bits in an IPv6 address?
5
How many usable hosts in a /24 subnet?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 14
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Answers
Digital Support and Security T Level · Network Design, Addressing and Transmission
14
1
What does load balancing do?
Spreads traffic across several servers.
2
Convert decimal 255 to binary.
11111111.
3
Why keep data cables away from power cables?
To avoid electromagnetic interference.
4
How many bits in an IPv6 address?
128.
5
How many usable hosts in a /24 subnet?
254.
Notes: Talk through any answers the class found difficult.

## Slide 15
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Activity: Subnet the office
Digital Support and Security T Level · Network Design, Addressing and Transmission
15
25 minutes
Individual
1
You have 192.168.10.0/24 for an office with four departments of up to 50 devices each.
2
Choose a subnet mask that gives four subnets.
3
Write the network address, first and last host and broadcast for each.
4
Suggest which resilience principle would protect the file server.
SUCCESS CRITERIA
Uses /26 correctly
Ranges do not overlap
Resilience choice is justified

## Slide 16
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Exit ticket
1
What is the difference between clustering and high availability?
2
Convert 1010 binary to decimal.
3
Name one improvement in Wi-Fi 6 over Wi-Fi 5.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Digital Infrastructure - Physical and Virtual Infrastructure
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/digital-infrastructure/02-physical-and-virtual-infrastructure.md
Notes: Students answer on a sticky note or in the chat before leaving.