## Slide 1
NETWORK CABLING
Testing, Certification and Troubleshooting
Network Cabling Content Area 2
Specification reference: 2.17, 2.18, 2.26 to 2.29
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
NETWORK CABLING · Network Cabling Content Area 2
Learning objectives
Digital Support and Security T Level · Testing, Certification and Troubleshooting
2
By the end of this lesson you should be able to:
1
Apply a troubleshooting process to cabling faults.
2
Identify common physical and technical failures.
3
Test and certify copper and fibre to recognised standards.
4
Explain the consequences of poor workmanship.
STARTER
A new desk outlet only connects at 100 Mbps instead of 1 Gbps. What could cause that?

## Slide 3
NETWORK CABLING · Network Cabling Content Area 2
Troubleshooting process
Digital Support and Security T Level · Testing, Certification and Troubleshooting
3
1
Identify
A fault, or found in routine monitoring.
2
Diagnose
Gather info, compare with past data, narrow down.
3
Test
Test the shortlist.
4
Resolve
Fix, document and prevent recurrence.
Maintenance can be predictive (replace before failure) or reactive (run to failure).

## Slide 4
NETWORK CABLING · Network Cabling Content Area 2
Common failures
Digital Support and Security T Level · Testing, Certification and Troubleshooting
4
Cabling faults are either physical or technical.
Physical faults include the wrong cable type, incorrect pin-out, open circuits (a broken wire), shorts, bad ports, bent pins, cable damage, duplex or speed mismatches and the wrong containment.
Technical faults include attenuation, latency, jitter, crosstalk, electromagnetic interference, mismatched transceivers, transmit and receive fibres reversed, bottlenecks and hardware errors.
They show up as CRC errors, lost frames and packets, address conflicts and missing sequence numbers. Status LEDs are often the first clue.
e.g.
EXAMPLE
A desk only connects at 100 Mbps instead of 1 Gbps. A test shows one pair broken: gigabit needs all four pairs, 100 Mbps only two.

## Slide 5
NETWORK CABLING · Network Cabling Content Area 2
Common failures
Digital Support and Security T Level · Testing, Certification and Troubleshooting
5
Physical
Wrong cable type or pin-out
Open or short circuit
Bad port, bent pins, cable damage
Duplex or speed mismatch
Wrong containment
Technical
Attenuation, latency, jitter
Crosstalk and EMI
Transceiver mismatch, TX/RX reversed
Bottlenecks and hardware errors
Spotted via CRC errors, lost packets, address conflicts

## Slide 6
NETWORK CABLING · Network Cabling Content Area 2
Quick check: Common failures
Digital Support and Security T Level · Testing, Certification and Troubleshooting
6
1
What is an open circuit?
2
What might cause CRC errors?
3
Why might a link fall back to 100 Mbps?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. A break in a wire so current can't flow.
2. E.g. interference, damaged cable, bad connectors.
3. E.g. a broken pair, since gigabit needs all four pairs.

## Slide 7
NETWORK CABLING · Network Cabling Content Area 2
Testing standards
Digital Support and Security T Level · Testing, Certification and Troubleshooting
7
Standard | Covers
TIA/EIA-568-B.2-1 | Cat6 transmission performance
TIA/EIA-568-B.1-10 | Augmented Cat6
TIA/EIA-TSB-155-A | Cat6 support for 10GBASE-T
TIA-1152 | Field test instrument requirements
IEC 61935-1 | Reference measurement procedures

## Slide 8
NETWORK CABLING · Network Cabling Content Area 2
Certifying copper and fibre
Digital Support and Security T Level · Testing, Certification and Troubleshooting
8
Certification proves an installation meets its standard, which the warranty depends on.
Follow a test plan setting out the scope, approach, resources and schedule. For copper, use a continuity tester, performance tester or cable certifier, checking the wiremap, cable length and near-end crosstalk (NEXT). For fibre, use an optical loss test set (light source and power meter), an OTDR and an inspection scope, running tier 1 (loss) and tier 2 (OTDR) tests.
Compare the results with the manufacturer's tolerances and record everything.
e.g.
EXAMPLE
A cable certifier reports one link at 94 m: over the 90 m permanent link limit, so it fails and the outlet must be moved or the route shortened.

## Slide 9
NETWORK CABLING · Network Cabling Content Area 2
Certifying copper and fibre
Digital Support and Security T Level · Testing, Certification and Troubleshooting
9
Copper
Continuity tester, performance tester, certifier
Wiremap
Cable length
Near-end crosstalk (NEXT)
Fibre
OLTS, light source and power meter
OTDR
Fibre inspection scope
Tier 1 and tier 2 testing
Notes: Follow a test plan (scope, approach, resources, schedule), then interpret results against manufacturer tolerances.

## Slide 10
NETWORK CABLING · Network Cabling Content Area 2
Quick check: Certifying copper and fibre
Digital Support and Security T Level · Testing, Certification and Troubleshooting
10
1
What does NEXT stand for?
2
What is a tier 1 fibre test?
3
Why does certification matter to customers?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. Near-end crosstalk.
2. A loss test with a light source and power meter.
3. It proves the installation meets the standard and supports the warranty.

## Slide 11
NETWORK CABLING · Network Cabling Content Area 2
Why poor workmanship matters
Digital Support and Security T Level · Testing, Certification and Troubleshooting
11
Cutting corners always costs more later.
For the network, poor workmanship means slower speeds, more interference, harder maintenance, shorter cable life and weaker security. Bad or missing labelling makes every future fault-find and change slower.
For the business, it means paying for revisits, penalties under the service level agreement and warranty, reputational damage, delayed payment and failed audits.
Not testing every cable risks equipment damage, early failures, disruption and errors nobody notices.
e.g.
EXAMPLE
An installer skips testing to finish early. Three months later, intermittent faults on six desks mean a return visit, unpaid, and an unhappy client.

## Slide 12
NETWORK CABLING · Network Cabling Content Area 2
Why poor workmanship matters
Digital Support and Security T Level · Testing, Certification and Troubleshooting
12
Network consequences
Slower speeds and more interference
Harder maintenance and shorter cable life
Weaker security
Bad labelling slows every future fault-find
Business consequences
Cost of revisits
SLA and warranty penalties
Reputational damage and delayed payment
Failed audits

## Slide 13
NETWORK CABLING · Network Cabling Content Area 2
Quick check: Why poor workmanship matters
Digital Support and Security T Level · Testing, Certification and Troubleshooting
13
1
Why does labelling matter?
2
Give two business consequences of poor workmanship.
3
Why test every cable, not a sample?
Answer on mini whiteboards or in your book. Answers are in the speaker notes.
Notes: Answers:
1. It makes fault-finding and changes much faster.
2. Any two: revisit costs, penalties, reputation, delayed payment, failed audits.
3. Untested faults cause failures and disruption later.

## Slide 14
NETWORK CABLING · Network Cabling Content Area 2
Check your understanding
Digital Support and Security T Level · Testing, Certification and Troubleshooting
14
1
What is the difference between predictive and reactive maintenance?
2
Name two physical cabling failures.
3
What does NEXT stand for?
4
Which tool locates a break along a fibre?
5
Give one business consequence of failing certification.
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 15
NETWORK CABLING · Network Cabling Content Area 2
Answers
Digital Support and Security T Level · Testing, Certification and Troubleshooting
15
1
What is the difference between predictive and reactive maintenance?
Predictive replaces before failure; reactive runs to failure.
2
Name two physical cabling failures.
Any two, e.g. wrong pin-out, open circuit, bent pins.
3
What does NEXT stand for?
Near-end crosstalk.
4
Which tool locates a break along a fibre?
An OTDR.
5
Give one business consequence of failing certification.
E.g. revisit costs, SLA penalties, reputational damage.
Notes: Talk through any answers the class found difficult.

## Slide 16
NETWORK CABLING · Network Cabling Content Area 2
Activity: Fault-find the patch leads
Digital Support and Security T Level · Testing, Certification and Troubleshooting
16
30 minutes
Pairs, practical
1
Test the six numbered patch leads your teacher provides.
2
Record the wiremap and length result for each.
3
Identify the fault in each failing lead.
4
Write a short certification summary for the passing leads.
SUCCESS CRITERIA
Every lead tested and recorded
Faults named correctly, e.g. split pair, open
Results compared with tolerances
Notes: Prepare leads with a split pair, a reversed pair, an open conductor and one good lead.

## Slide 17
NETWORK CABLING · Network Cabling Content Area 2
Exit ticket
1
Why must every cable be tested, not just a sample?
2
What might cause a CRC error?
3
Why does labelling matter?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Network Cabling - Installation and Testing
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/network-cabling/02-cabling-installation-and-testing.md
Notes: Students answer on a sticky note or in the chat before leaving.