## Slide 1
NETWORK CABLING
Signal Theory and Data Transmission
Network Cabling Content Area 2
Specification reference: 2.1, 2.7 to 2.10
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
NETWORK CABLING · Network Cabling Content Area 2
Learning objectives
Digital Support and Security T Level · Signal Theory and Data Transmission
2
By the end of this lesson you should be able to:
1
Describe how data is represented, encapsulated and transmitted.
2
Explain total internal reflection and single-mode and multi-mode fibre.
3
Explain the causes of attenuation and the effects of poor fibre handling.
4
Apply Ohm's law to copper cabling.
STARTER
Shine a torch down a long clear pipe. Why does less light come out of the far end?

## Slide 3
NETWORK CABLING · Network Cabling Content Area 2
Principles of data transmission
Digital Support and Security T Level · Signal Theory and Data Transmission
3
Data is represented as bits, bytes and packets.
Transmission is synchronous or asynchronous.
Links must handle error detection and correction, bandwidth limits, noise and compression.
Access methods: CSMA/CD on wired networks, CSMA/CA on wireless.
The NIC encapsulates data into frames, packets and datagrams with addresses and sequence numbers.
!
KEY IDEA
Addressing: IPv4 (schemes, subnetting, masks) and IPv6 (address types).

## Slide 4
NETWORK CABLING · Network Cabling Content Area 2
How fibre carries light
Digital Support and Security T Level · Signal Theory and Data Transmission
4
Total internal reflection
Light travels down the glass core
It reflects off the boundary with the cladding
Refraction principles keep it inside the core
Single-mode and multi-mode
Single-mode: one ray, narrow core, long distance
Multi-mode: many rays, wider core, shorter distance

## Slide 5
NETWORK CABLING · Network Cabling Content Area 2
Attenuation: losing signal over distance
Digital Support and Security T Level · Signal Theory and Data Transmission
5
1
Measured in dB
Loss of signal strength along the cable.
2
Absorption
Light absorbed by particles in the glass; worse over distance.
3
Scattering
Light hits particles and is lost into the cladding.
4
Bending
Macrobends and microbends let light escape.
Notes: Poor handling faults: dirty or damaged connectors (unreliable or no link), bending too tightly, and poor-quality cable or connectors.

## Slide 6
NETWORK CABLING · Network Cabling Content Area 2
Ohm's law and copper cabling
Digital Support and Security T Level · Signal Theory and Data Transmission
6
V = I x R: voltage equals current times resistance.
More voltage gives more current.
More resistance gives less current.
Resistance rises with cable length, signal frequency and smaller cable size.
!
KEY IDEA
Resistance is why copper has a maximum length: 90 m permanent link and 100 m total channel.
Notes: Worked example: 12 V across 4 ohms gives 3 A. Double the resistance and the current halves.

## Slide 7
NETWORK CABLING · Network Cabling Content Area 2
Check your understanding
Digital Support and Security T Level · Signal Theory and Data Transmission
7
1
What does CSMA/CD stand for?
2
What keeps light inside a fibre core?
3
Which fibre type suits long distances?
4
Name two causes of attenuation.
5
Using V = I x R, what current flows with 10 V and 5 ohms?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
NETWORK CABLING · Network Cabling Content Area 2
Answers
Digital Support and Security T Level · Signal Theory and Data Transmission
8
1
What does CSMA/CD stand for?
Carrier Sense Multiple Access with Collision Detection.
2
What keeps light inside a fibre core?
Total internal reflection.
3
Which fibre type suits long distances?
Single-mode.
4
Name two causes of attenuation.
Any two of: absorption, scattering, macrobending, microbending.
5
Using V = I x R, what current flows with 10 V and 5 ohms?
2 amps.
Notes: Talk through any answers the class found difficult.

## Slide 9
NETWORK CABLING · Network Cabling Content Area 2
Activity: Signal loss investigation
Digital Support and Security T Level · Signal Theory and Data Transmission
9
25 minutes
Pairs
1
Use the fibre loss figures given by your teacher for three links.
2
Identify which link has a fault, and the most likely cause.
3
Calculate current for three copper examples using Ohm's law.
4
Explain why a 150 m copper run would be a problem.
SUCCESS CRITERIA
Faulty link found with evidence
Calculations correct with units
Maximum length explained using resistance

## Slide 10
NETWORK CABLING · Network Cabling Content Area 2
Exit ticket
1
Why is multi-mode fibre used for short runs?
2
What happens to current if resistance increases?
3
Name one way poor handling damages fibre.
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Network Cabling - Installation and Testing
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/network-cabling/02-cabling-installation-and-testing.md
Notes: Students answer on a sticky note or in the chat before leaving.