## Slide 1
NETWORK CABLING
Health, Safety and Compliance for Cabling
Network Cabling Content Area 2
Specification reference: 2.19 to 2.24
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
NETWORK CABLING · Network Cabling Content Area 2
Learning objectives
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
2
By the end of this lesson you should be able to:
1
Identify supporting media and how to protect it during installation.
2
Describe the standards and legislation that govern cabling work.
3
Respond correctly to suspected asbestos.
4
Apply risk management to working at height and in confined spaces.
STARTER
You lift a ceiling tile and see old, crumbly grey board. What should you do?

## Slide 3
NETWORK CABLING · Network Cabling Content Area 2
Protecting supporting media
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
3
Supporting media: telecoms, CCTV, alarms, AV, wireless access points, IoT devices.
Avoid sharing containment routes with other services.
Label service cables.
Check local records before starting.
Apply change management.
!
KEY IDEA
Segregate data cables from electrical cables in line with BS EN 50174.

## Slide 4
NETWORK CABLING · Network Cabling Content Area 2
Key cabling standards
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
4
Standard | Covers
BS EN 50173 / ISO/IEC 11801 | Generic cabling systems
BS EN 50174 | Installation specification and quality
BS EN 50310 | Bonding and earthing
BS EN 60825 | Optical fibre safety
BS 6701 and BS 7671 | Installation and wiring regulations
IEEE 802.3 / 802.16 | Ethernet / WiMAX
TIA/EIA-568-B, IEC 60364 | Cable categories; electrical installations

## Slide 5
NETWORK CABLING · Network Cabling Content Area 2
Legislation
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
5
1
HSWA 1974
The general duty of care.
2
Electricity at Work 1989
Safe work near electrical systems.
3
Work at Height 2005
Planning and equipment for work at height.
4
COSHH 2002
Hazardous substances.
5
Confined Spaces 1997
Safe entry and rescue plans.
6
PPE 2018 and Asbestos 2012
Protective equipment; control of asbestos.

## Slide 6
NETWORK CABLING · Network Cabling Content Area 2
If you suspect asbestos
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
6
1
Stop
Stop work immediately.
2
Inform
Tell the relevant people.
3
Isolate
Restrict access to the area.
4
Investigate
Use an asbestos-registered professional.
5
Act
Removal, sealing or air-quality checks.

## Slide 7
NETWORK CABLING · Network Cabling Content Area 2
Working at height and in confined spaces
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
7
At height
Risk assess before starting
Use MEWPs safely
Assemble, inspect and dismantle towers per the manufacturer
Record findings
Confined spaces
Same risk management process
Correct PPE, properly maintained
Plan for rescue
Record findings clearly

## Slide 8
NETWORK CABLING · Network Cabling Content Area 2
Check your understanding
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
8
1
Which standard covers segregation of data and power cables?
2
What is the first thing to do if you suspect asbestos?
3
Which regulations cover work in ceiling voids and ducts?
4
Which standard covers optical fibre safety?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 9
NETWORK CABLING · Network Cabling Content Area 2
Answers
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
9
1
Which standard covers segregation of data and power cables?
BS EN 50174.
2
What is the first thing to do if you suspect asbestos?
Stop work immediately.
3
Which regulations cover work in ceiling voids and ducts?
Confined Spaces Regulations 1997.
4
Which standard covers optical fibre safety?
BS EN 60825.
Notes: Talk through any answers the class found difficult.

## Slide 10
NETWORK CABLING · Network Cabling Content Area 2
Activity: Method statement
Digital Support and Security T Level · Health, Safety and Compliance for Cabling
10
30 minutes
Small groups
1
Scenario: run 20 new cables through a 1970s school corridor ceiling, 3.5 m high.
2
Write a method statement with a risk assessment.
3
Name the legislation and standards that apply at each step.
4
Include what to do if ACM or live services are found.
SUCCESS CRITERIA
Height and asbestos risks covered
Correct legislation named
Clear stop and escalate steps

## Slide 11
NETWORK CABLING · Network Cabling Content Area 2
Exit ticket
1
Why must you check local records before drilling?
2
Name one piece of access equipment and its main hazard.
3
Who can investigate suspected asbestos?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Network Cabling - Installation and Testing
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/network-cabling/02-cabling-installation-and-testing.md
Notes: Students answer on a sticky note or in the chat before leaving.