## Slide 1
DIGITAL INFRASTRUCTURE
Infrastructure Components and Cabling
Digital Infrastructure Content Area 2
Specification reference: 2.3, 2.15
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Learning objectives
Digital Support and Security T Level · Infrastructure Components and Cabling
2
By the end of this lesson you should be able to:
1
Describe the purpose of common network and end-user devices.
2
Compare storage options, including RAID levels, NAS and SAN.
3
Describe cabling, connectors, antennas and test equipment.
4
Make and test a UTP cable to TIA/EIA standards.
STARTER
What is the difference between a hub, a switch and a router? Have a guess before we look.

## Slide 3
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Network devices
Digital Support and Security T Level · Infrastructure Components and Cabling
3
Device | What it does
Firewall (NGFW / UTM) | Filters traffic; next-generation and unified threat management add deeper inspection
Router | Forwards packets between networks
Switch | Connects devices in a LAN and sends frames only to the right port
Hub / bridge | Hub repeats to every port; bridge joins two segments
Wireless access point / extender | Provides and extends Wi-Fi coverage
Modem / media converter | Connects to the ISP; converts between copper and fibre

## Slide 4
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Storage
Digital Support and Security T Level · Infrastructure Components and Cabling
4
1
HDD, SSD, removable
Cheap capacity, fast solid state, or portable media.
2
NAS and SAN
File storage on the network, or a dedicated block storage network.
3
Block and object
Raw blocks for databases; objects with metadata for cloud storage.
4
RAID 0 and 1
0 stripes for speed with no redundancy; 1 mirrors for safety.
5
RAID 5 and 10
5 uses parity across three or more disks; 10 mirrors and stripes.

## Slide 5
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Wired and wireless technology
Digital Support and Security T Level · Infrastructure Components and Cabling
5
1
UTP cabling
Straight-through or crossover, wired to TIA/EIA-568A or B.
2
Connectors
RJ45 for Ethernet, RJ11 for telephone.
3
Cable types
Copper Cat5e and Cat6, or fibre optic.
4
Protocols
PPP, software-defined networking, WPA1, 2 and 3.
5
Antennas
Omni-directional, directional, patch, yagi and dipole.
6
Test equipment
Tone generator and probe, cable tester, tracing kit, test plans.
Notes: Also in 2.3: cloud service models (IaaS, PaaS, SaaS), scripting for automation, network monitoring and capacity management.

## Slide 6
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Making and testing a UTP cable
Digital Support and Security T Level · Infrastructure Components and Cabling
6
1
Plan
Decide the purpose and calculate the length.
2
Choose
Straight-through or crossover.
3
Prepare
Strip and order the wires to 568A or 568B.
4
Crimp
Fit 8P8C (RJ45) connectors with a crimper.
5
Test
Check wiremap and continuity against TIA/EIA.

## Slide 7
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Check your understanding
Digital Support and Security T Level · Infrastructure Components and Cabling
7
1
What does a switch do that a hub does not?
2
Which RAID level offers no redundancy?
3
Which connector is used for Ethernet?
4
What is a crossover cable?
5
Which antenna type sends signal in all directions?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Answers
Digital Support and Security T Level · Infrastructure Components and Cabling
8
1
What does a switch do that a hub does not?
Sends frames only to the port of the destination device.
2
Which RAID level offers no redundancy?
RAID 0.
3
Which connector is used for Ethernet?
RJ45 (8P8C).
4
What is a crossover cable?
A cable wired 568A at one end and 568B at the other.
5
Which antenna type sends signal in all directions?
Omni-directional.
Notes: Talk through any answers the class found difficult.

## Slide 9
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Activity: Make a patch lead
Digital Support and Security T Level · Infrastructure Components and Cabling
9
40 minutes
Practical, individual
1
Measure and cut a 1 metre length of Cat6 UTP.
2
Terminate both ends to TIA/EIA-568B.
3
Test it with a cable tester and record the wiremap result.
4
If it fails, find the fault, re-terminate and retest.
SUCCESS CRITERIA
Correct colour order at both ends
Jacket crimped inside the connector
Test result recorded
Safe use of tools
Notes: Wear eye protection when cutting. Keep offcuts for fault-finding practice.

## Slide 10
DIGITAL INFRASTRUCTURE · Digital Infrastructure Content Area 2
Exit ticket
1
When would you choose RAID 10 over RAID 5?
2
What does a media converter do?
3
What does a wiremap test check?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Digital Infrastructure - Physical and Virtual Infrastructure
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/digital-infrastructure/02-physical-and-virtual-infrastructure.md
Notes: Students answer on a sticky note or in the chat before leaving.