## Slide 1
NETWORK CABLING
Structured Cabling Design and Installation
Network Cabling Content Area 2
Specification reference: 2.2 to 2.6, 2.25
Digital Support and Security T Level · Lesson slides
Unofficial teaching resource. Check the official Pearson specification for assessment detail.

## Slide 2
NETWORK CABLING · Network Cabling Content Area 2
Learning objectives
Digital Support and Security T Level · Structured Cabling Design and Installation
2
By the end of this lesson you should be able to:
1
Select tools and equipment for testing, terminating and access.
2
Install and configure networking devices to a design specification.
3
Describe what a network design specification contains.
4
Install fixtures and fittings such as cabinets, racks and containment.
STARTER
You arrive at a new building to install a network. What documents would you want in your hand before you start?

## Slide 3
NETWORK CABLING · Network Cabling Content Area 2
Tools and equipment
Digital Support and Security T Level · Structured Cabling Design and Installation
3
1
Testing
Multimeter, tone generator and probe, OTDR, light source and power meter, spectrum analyser, continuity tester.
2
Terminating
Crimper, strippers, cutters, punch-down tool, fusion splicer, fibre cleaning and cleave tools.
3
Access
MEWPs, low-level access towers, step ladders.
4
Fixtures
Prebuilt or flat-pack cabinets, racks, trunking and containment.
Notes: Students assess the job, select the right tool and use it safely per manufacturer guidance.

## Slide 4
NETWORK CABLING · Network Cabling Content Area 2
Installing a networking device
Digital Support and Security T Level · Structured Cabling Design and Installation
4
1
Locate
Find its position in the design spec.
2
Check
Equipment matches the spec.
3
Fit
Confirm space, power and cooling.
4
Rack
Mount the device.
5
Test
Check it works.
6
Configure
Set it up to the requirement.
Notes: Devices include firewalls, routers, switches with SFP modules, access points, VoIP endpoints, CCTV and servers.

## Slide 5
NETWORK CABLING · Network Cabling Content Area 2
The network design specification
Digital Support and Security T Level · Structured Cabling Design and Installation
5
1
Statement of requirement
What the customer needs.
2
Bill of materials
Every component and quantity.
3
Design documents
Floor plans, power and cooling, containment, cable routes.
4
Installation admin
Labelling, certification, warranty, performance declarations.
5
Procedures and penalties
How to install, and contractual penalties.
6
Future proofing
Room to grow.
Notes: Design is shaped by logical and physical topology, standards, permanent links and channels, campus distribution and passive and active design.

## Slide 6
NETWORK CABLING · Network Cabling Content Area 2
Installing fixtures and fittings
Digital Support and Security T Level · Structured Cabling Design and Installation
6
1
Interpret
Read the cabling design spec.
2
Survey
Compare the site: space, power, cooling.
3
Build
Construct cabinets and racks per manufacturer guidance.
4
Contain
Add trunking and containment.
5
Arrange and test
Lay out kit to spec and test compliance.

## Slide 7
NETWORK CABLING · Network Cabling Content Area 2
Check your understanding
Digital Support and Security T Level · Structured Cabling Design and Installation
7
1
What does an OTDR test?
2
What is a bill of materials?
3
What three things must be checked before racking a device?
4
What is a MEWP?
Notes: Give students a few minutes to answer on mini whiteboards or paper, then reveal the answers on the next slide.

## Slide 8
NETWORK CABLING · Network Cabling Content Area 2
Answers
Digital Support and Security T Level · Structured Cabling Design and Installation
8
1
What does an OTDR test?
Fibre links, locating faults and loss along the cable.
2
What is a bill of materials?
A list of every component and quantity needed.
3
What three things must be checked before racking a device?
Space, power and cooling.
4
What is a MEWP?
A mobile elevating work platform.
Notes: Talk through any answers the class found difficult.

## Slide 9
NETWORK CABLING · Network Cabling Content Area 2
Activity: Read the design spec
Digital Support and Security T Level · Structured Cabling Design and Installation
9
30 minutes
Small groups
1
Study the sample floor plan and statement of requirement from your teacher.
2
Calculate cable lengths and quantities for each outlet.
3
Produce a bill of materials.
4
Flag three potential issues with the design.
SUCCESS CRITERIA
Lengths include slack and stay under 90 m
Bill of materials is complete
Issues are realistic and explained

## Slide 10
NETWORK CABLING · Network Cabling Content Area 2
Exit ticket
1
Why is future-proofing part of the design?
2
Name one terminating tool for fibre.
3
What goes on a label at a patch panel?
REVISE THIS TOPIC
Revision notes for this lesson are on the study wiki:
Network Cabling - Installation and Testing
https://lana6478.github.io/Digital-Suport-and-security-T-levle/#/02-occupational-specialisms/network-cabling/02-cabling-installation-and-testing.md
Notes: Students answer on a sticky note or in the chat before leaving.